## Slide 1: SABD Project #2
Real-Time Defect Detection in L-PBF Manufacturing Using Stream Processing with Apache Flink
Macroarea di Ingegneria
Dipartimento di Ingegneria Civile e Ingegneria Informatica
Corso di Sistemi e Architetture per Big Data
Laurea Magistrale in Ingegneria Informatica
A.A. 2024/25
Matteo Basili, Adriano Trani

## Slide 2: Outline
Goals
Introduction & Background
Overview
Data Acquisition and (Kafka) Ingestion
Implementation of Queries (Flink)
Results
Performance Analysis and Discussion
Demo

## Slide 3: Goals
Analyze real-time thermal images from L-PBF additive manufacturing using DEBS 2025 dataset
Develop a distributed stream processing pipeline to:
Retrieve, process and analyze data
  Answer specific queries
  Export results
Measure latency and throughput for each query
Present and discuss the results and system performance

## Slide 4: Introduction & Background
Laser Powder Bed Fusion (L-PBF) is a 3D printing technology that builds metal parts layer by layer using a high-power laser
Enables complex geometries and reduces material waste compared to subtractive methods
Quality issues (e.g., porosity, thermal instabilities) can affect part integrity and are traditionally detected post-production
Real-time defect detection can reduce waste and improve reliability
Optical Tomography (OT) captures high-resolution thermal images during the printing process
These images represent temperature distribution across the powder bed for each layer

## Slide 5: Dataset
Provided by ACM DEBS 2025 Grand Challenge as a continuous stream via a REST-based LOCAL-CHALLENGER
Organized by layers (z-axis)
Each layer divided into tiles (sub-images)
Each tile is a temperature map: pixels represent temperature values (0–65,535)
Each element of the data stream includes:
  seq_id: Sequence number
  print_id: Printed object ID
  tile_id: Tile identifier
  layer: Z-coordinate
  tiff: Binary temperature image

## Slide 6: Queries
Q1 – Saturation Analysis
  Identify pixels in each tile with:
Tp < 5,000 → void areas (excluded from further analysis)
    Tp > 65,000 → saturated pixels (potential defects)
  Count the number of saturated points
Q2 – Outlier Detection
  Sliding window over last 3 layers
  For each pixel in the newest layer:
    Compute local temperature deviation =
    | avg(inner neighbors) - avg(outer neighbors) |
    Mark as outlier if deviation > 6,000
  Output top-5 points with highest local temperature deviation per tile
Q3 – Outlier Clustering
  Apply DBSCAN clustering on Q2 outliers (Euclidean distance) to compute cluster centroids and sizes
  Output sent to Local-Challenger for performance evaluation
Q1
Q2
Q3
Data flow
Output

## Slide 7: Overview - Technology Stack
Docker & Docker Compose: Containerization of the entire system
Apache Flink: Processing the data
Apache Kafka: Message brokering between components
Python: Main programming language

## Slide 8: Overview - Architecture

## Slide 9: Overview - DataFlow
Client establishes a session with the LOCAL-CHALLENGER and starts the benchmark
OT image tiles are fetched in real time from the LOCAL-CHALLENGER stream
Retrieved tiles are published to a Kafka topic for processing
Flink consumes the tiles and executes the multi-stage analysis pipeline
Query results are written to dedicated Kafka output topics
Client consumes Q3 outputs from Kafka
Q3 results are sent to the LOCAL-CHALLENGER to complete the benchmark
The LOCAL-CHALLENGER evaluates and returns performance metrics (latency, throughput)

## Slide 10: Overview - Docker Containers
The system is fully containerized with Docker and orchestrated using Docker Compose
  LOCAL-CHALLENGER: local-challenger
  Flink: jobmanager, taskmanager1, taskmanager2
  Kafka: zookeeper, kafka1, kafka2, topic-init
  Client: l-pbf-client
  Results exporter: csv-writer

## Slide 11: Client – Data Acquisition and Ingestion
Client continuously requests image batches from the LOCAL-CHALLENGER platform via REST API
The data is published to the Kafka topic tiff-batches, which serves as the input stream for the Flink pipeline
A dedicated Kafka producer thread handles batch publishing

## Slide 12: Implementation – Q1

## Slide 13: Implementation – Q2

## Slide 14: Implementation – Q3

## Slide 15: Client – Results collection
A Kafka consumer runs in a separate thread, continuously listening to the Q3 output topic (l-pbf-output)
Each message is sent via REST to LOCAL-CHALLENGER for validation
When all batches are received, the client:
  Finalizes the benchmark
  Triggers LOCAL-CHALLENGER to return application performance metrics (latency, throughput, etc.)
l-pbf_client.py script

## Slide 16: Results – Export
The CSV Writer ingests streaming data from multiple Kafka topics and writes them to corresponding CSV files in real time
Uses Kafka consumers, spawning one thread per topic for concurrent consumption
Each message is parsed as a CSV string and appended to a query-specific file
Output:
  Q1: seq_id, print_id, tile_id, saturated
  Q2: seq_id, print_id, tile_id, p_1, dp_1, p_2, dp_2, p_3, dp_3, p_4, dp_4, p_5, dp_5
  Q3: seq_id, print_id, tile_id, saturated, centroids
kafka_to_csv_stream_writer.py script

## Slide 17: Results - Example
Q3 output

## Slide 18: Performance Analysis – Setup
Apache Flink (default) configuration
  Parallelism: set to 1
    → Each operator runs as a single task
Kafka Topics:
  Single-partition
    → One Flink subtask per topic → no parallel reads
  Replication factor = 2
    → Basic fault tolerance
Rationale:
  Simplified setup for baseline performance evaluation
  Avoids noise from parallelism and tuning overhead

## Slide 19: Performance Analysis – Execution Logic
Custom log lines emitted by each query with batch ID and latency:
METRICS|Q1|batch=123|latency_ms=17.46
Implemented via manual timestamp logging in each query function
analyze_latency.py script
  Log parsing
  Latency stats
    Mean, max, p50/p90/p99, batch counts
  Throughput estimation
    Batches processed / total run time
  Excel export
3 runs
  100, 200 and 300 batches

## Slide 20: Performance Analysis – Results
Q1 | Mean Latency (ms) | Max Latency (ms) | Latency Perc 50 (ms) | Latency Perc 90 (ms) | Latency Perc 99 (ms) | Throughput (batch/s)
100 batch | 58.7562 | 942.16 | 22.14 | 80.521 | 711.49 | 0.352939
200 batch | 87.36195 | 2535.01 | 27.085 | 83.67 | 1506.5952 | 0.233359
300 batch | 100.7782 | 2081.97 | 31.23 | 128.08 | 1606.7608 | 0.244792
Q2 | Mean Latency (ms) | Max Latency (ms) | Latency Perc 50 (ms) | Latency Perc 90 (ms) | Latency Perc 99 (ms) | Throughput (batch/s)
100 batch | 3390.3514 | 10696.52 | 3212.92 | 8266.299 | 9991.9865 | 0.352274
200 batch | 4280.8253 | 11439.79 | 3743.695 | 8620.857 | 10433.9657 | 0.232865
300 batch | 4711.088267 | 12825.29 | 4095.37 | 8836.136 | 11893.4476 | 0.244775
Q3 | Mean Latency (ms) | Max Latency (ms) | Latency Perc 50 (ms) | Latency Perc 90 (ms) | Latency Perc 99 (ms) | Throughput (batch/s)
100 batch | 9.129 | 592.46 | 0.06 | 9.117 | 76.8383 | 0.269552
200 batch | 5.09805 | 440.77 | 1.3 | 7.424 | 17.7009 | 0.225976
300 batch | 5.2814 | 493.82 | 2.52 | 8.68 | 29.8744 | 0.207425

## Slide 21: References
https://github.com/MatteoBasili/sabd-progetto2-2024_25

## Slide 22: Demo
Open terminal
Enter the root directory of the project
Launch containers
  $ docker compose up --build –d
Execute the full pipeline
  $ python3 ./scripts/run_all.py [--limit N]
Check the results (CSV files) in the directory Results/csv